   MMMM MMMM CCCCCCCC EEEEEEEEEE
   MM MM MM MM CCC CCC EE EEE
   MM MM MM MM CC CC EE
   MM MMM MM CC EEEEEEE
   MM M MM CC EEEEEEE
   MM MM CC CC EE
   MM MM CCC CCC EE EEE
   MM MM CCCCCCCC EEEEEEEEEE

COMMAND LINE EDITOR

This manual describes MCE V4.29 for RSX180
from September 2018

originally developed by

D. Sponza (YU) Oct-81

Since 29-Jul-86 Supported by

Hans Hamakers
pAkUiT International
Elsbes 40 , 3069 LN Rotterdam
The Netherlands

Table of Contents

# Introduction
MCE is an RSX180 task through which you can communicate with the CLI (Command Line Interpreter, e.g. MCR or DCL) currently active at your terminal.

MCE lets you edit your command lines in an EDT-like way in keypad or non-keypad mode. MCE stores the command lines for you in a FIFO-buffer for later retrieval. In addition, you can define your own commands in the same way as in OpenVMS.
# Options

Below are listed the optional features supported by MCE. They can individually be selected at build time.
- Multiple CLI support
- Init-File support
- Compound Command Line support
- Status Line support
- Startup and Exit messages
- Remote Terminal (RT: and HT:) detection
- VT2plus support[1]
  [1] In this manual VT2plus means support for VT2xx, VT3xx, VT4xx and VT5xx terminals.
- VT4plus support[2]
  [2] In this manual VT4plus means support for VT4xx, and VT5xx terminals.
- TDV2230 Function Key support
- EDT-Keypad editing support
- User Prompt support
- Extended Prompt support
- Terminal Password Locking
- Automatic return to Insert or Overwrite mode
- Terminal Time-Out support
## Multiple CLI support
When multiple CLI support is included, MCE uses the prompt from the CLI that is active at the invoking terminal. Furthermore, different Init-Files for MCR, DCL or other CLIs can exist.
## Init-File support
When Init-File support is included, MCE reads initialization files which can contain Command Synonym definitions, Internal- and CLI-commands. Files are searched in this order:
When multiple CLI support is included:
LB:[1,2]MCEINI.xxx, followed by
SY:[CurDir]MCEINI.xxx or SYS$LOGIN:MCEINI.xxx

When multiple CLI support is not included:
LB:[1,2]MCEINI.CMD, followed by
SY:[CurDir]MCEINI.CMD or SYS$LOGIN:MCEINI.CMD

where “xxx” is the name of the CLI defined for the terminal invoking MCE and “CurDir” is the default directory at the startup of MCE.
This algorithm divides command definition into two groups: A system-wide set in LB:[1,2] followed by users private set in SY:[CurDir] or SYS$LOGIN:
MCE can be configured to always read the user Init-File from SYS$LOGIN: on systems that support Logical Names (Only possible on M-Plus). This makes you independent from where you start MCE.
Overriding the default filename in the Command Line which invokes MCE offers the possibility to tailor an application specific command set.
Comments are possible behind “!” which is the comment character for CLI’s.
An Example of an Init-File can be found in Appendix A.
## Compound Command Line support
MCE allows definitions of compound commands. Using the ampersand sign “&”, an MCE command can be defined as a sequence of multiple CLI commands, for example:
 +>STAT := TIM & PIP /LI & ACT /ALL ... etc.

This defines STAT as a sequence of CLI commands that are executed one after another. MCE waits for completion of one command before activating the next.
It can also be done directly, e.g.:
+>MAC @TASKASM & TKB @TASKTKB

The “&” MUST be preceded by at least one space. This is done to let commands like “PIP /TD&/LI” still work.
When a command in a compound command line gives a non-successful exit status, MCE terminates the compound command line there, showing the exit status and the command that caused it.
A compound command line may also contain Internal Commands (Commands starting with “MCE”) in mixture with normal CLI commands. Only the first command is checked for translation.
## Status Line support
Line 24 on an ANSI CRT terminal can be used for status information. The Status Line shows the different settings and FIFO-buffer parameters of MCE, and can be switched on or off with MCE STATus ON|OFF. For non ANSI terminals like VT52’s, only a snapshot can be displayed with MCE STATus.

The Status Line displays the following information:
MCE-V4.29 FIFO:list/22/16/00 CMSZ:04 KEYP:on SVINT:off SVOLD:on TMO:xx

Time-Out time
in minutes,
“off” or “no”

Save old cmds
“on” or off”

 Save intern cmds
“on” or “off”

Keypad editing “on” or
“off”

Minimum
size of Command Line

Number of current cmdline from FIFO

Number of cmdlines in FIFO

Maximum number of cmdlines in FIFO

FIFO is a “list” or a “ring”

MCE Version

## Startup and Exit messages
The Startup and Exit messages like:
MCE -- CLI Command Line Editor V4.29
and
MCE – Exit

are optional. They can be enabled or disabled at build time.

MCE identifies itself with:
MCE -- MCR Command Line Editor V4.29

when no multiple CLI support was selected at build time.
## Remote terminal (RT: and HT:) detection
When MCE is started via a remote terminal, problems can occur if the local system is VMS with its Command Line Editor enabled. The way MCE acts when it detects if it is started via a remote terminal can be specified at build time. One of the following options can be selected:
Give the following message:

MCE -- ** WARNING ** Started on a Remote Rerminal.
       If your local system is OpenVMS with its Command Line
       Editor enabled please type “MCE EXIT”

Give the following message and exit:

MCE -- Started on a Remote Terminal, exiting...

Do nothing.
## VT2Plus support
VT2plus support enables the use of VT2+[3] keyboards.
[3] VT2+ in this manual stands for VT2xx and later models.
The keys <F11>, <F12> and <F13> work as <ESC>, <BS> and <LF>. The keys <HELP>, <DO> etc. can also be used and it is possible to define the Function Keys <F6>..<F20> like
F6 := TIM

Pushing <F6> then gives the time of day (see Function Keys).
## VT4plus support
On a VT4+[4] terminal it is possible to use <F1>..<F5> as normal Function Keys. MCE allows you to define those keys in the same way as other Function Keys when this support is included with MCEBLD.
[4] VT4+ in this manual stands for VT4xx and later models.
## Tandberg TDV2230 function key support
The keys of a Tandberg TDV2230 terminal can be defined like the ones on a VT2+. (See Function Keys).
## EDT-Keypad editing support
Some edit functions can be performed on a VT52/VT1xx/VT2+-keypad, similar to K52, KED and EDT. The Keypad-editing can be switched on or off with MCE KEYPad ON|OFF.
## User Prompt support
The MCE prompt can be specified by the user with MCE USPRompt UserPrompt. A User Prompt can contain up to 20 characters.
The return to the default prompt type MCE USPRompt.
## Extended Prompt support
The MCE prompt can show if Insert or Overwrite mode is active with “+” or “‑” respectively. It can also display if keypad editing is enabled when the Status Line is off with “:”, for example:
+:>
The Extended Prompt can be switched on or off with MCE PROMpt ON|OFF.
## Terminal password locking
When selected, this option enables the MCE LOCK command. It prompts for a password and verification and locks the terminal. When the password is entered again the terminal is ready to use again.
This is all like the LOCK command from Digital’s Terminal servers.
## Automatic return to Insert or Overwrite mode
Default Insert or Overwrite mode stays active until it is changed with <CTRL/A> or <F14>. MCE can be built so that it sets one of the modes active by default when it prompts for a new command. This can be changed with the MCE INSErt ON|OFF and MCE OVERstrike ON|OFF commands.
## Terminal Time-Out support
When terminal Time-Out support is included and the terminal is not used within a given time the terminal is logged-out (at TT0: MCE only exits).
Optionally the time-out value can be changed with MCE TIMOut nnn to be 2 to 999 minutes or can be enabled or disabled with the MCE TIMOut ON|OFF command. The MCE TIMOut command MUST be included during build time to let this work (so system managers, do not be afraid, if YOU do not want it, they will not get it).
# Startup and Exit
## Command Line Editor Startup
Invoke MCE with command “MCE”, preferably from your LOGIN file with a “.XQT MCE” statement. If Init-File support is included, a file of Command-Synonyms, CLI-Commands, and/or Internal-Commands will be read and executed during MCE startup. The file may be specified in the form “MCE <startup-file>”. If no startup file is specified in the command line (the normal case), the default Init-Files are searched for (see Init-Files).
## Command Line Editor Exit
To exit MCE use the MCE EXIT internal command or <CTRL/Y>.
# Command Lines
When MCE is ready to accept a command line it displays a prompt. How the prompt looks depends on the chosen options and setup of MCE (see Extended Prompt). The maximum length of command lines is 78 characters.
If a command line starts with “MCE”, it is interpreted as an Internal Command. Other command lines are checked for translation and the result is spawned to the current CLI.
Special action is performed with “BYE” and “LOG[out]”. “BYE”, and when in DCL “LOG[out]” result in a spawn of “BYE” to MCR and MCE exits immediately. Note that you may define any other string (e.g. “GOODBYE”) to result in “BYE” or “LOGOUT”.
All command lines can be preceded by and contain one or more TAB’s and/or spaces.
Normally all command lines equal to or longer than a given length are saved in a FIFO-buffer. This length can be changed with the MCE CMSZ n command.
The maximum number of command lines the FIFO-buffer can hold can be specified with the MCE FISZ n command. When the maximum number of command lines is present, or when no buffer pool space is available to hold more entries, the new command line is saved and the oldest disappears.
Retrieved command lines from the FIFO-buffer are only saved again if they are edited or when the saving of “old” command lines is enabled by MCE SVOLd ON and this command line is not the newest in the FIFO. This prevents filling up your FIFO with one command by continuously repeating the last command.
Internal commands are saved when this is enabled by MCE SVINternals ON (save “INTERNAL” commands).
# Command synonyms
A command synonym can be defined with:
+>Syn := <Command1> [ & <Command2> [ & ... ] ].

where “Syn” is the command synonym which will be substituted by the text at the right side of “:=”, e.g.:
+>HE := HELP PIP
+>HE	will request “HELP PIP”

Note: The “:=” must be preceded and followed by at least one TAB or space.
With Keypad-mode “OFF” the keystrokes <PF1> , <BLUE> or <ESC>P translate the command synonym without execution.
If you enter a command synonym followed by additional text, this additional text will normally be appended as a whole.
e.g.:	+>HE /RE	Will request “HELP PIP /RE”
or	+>HE /RE<PF1>	Will be translated and displayed
result:	+>HELP PIP /RE

A command synonym can be deleted by redefining it to null, e.g.:
+>HE :=	Delete above definition

Abbreviate commands by separating the optional part by “*”, e.g.:
+>HP*IP := HELP PIP

This command can now be requested with:
+>HP or HPI or HPIP etc.

More sophisticated is the Parameter Substitution, similar to the indirect command file processor:
+>DIR*ECTORY	:= PIP ‘P1’/LI
+>COP*Y	:= PIP ‘P2’/NV/CD=’P1’

+>DIR	Will be translated into “PIP /LI”
+>DIREC FIL	Will be translated into “PIP FIL/LI”
+>COPY A.CMD [1,2]	Will simulate the DCL COPY command

Note that command synonyms may be executed from Init-Files as well.
# Function Keys
You can request a command with Function Keys <PF1>, <PF2>, <PF3> or <PF4>.
The keys <BLUE>, <RED> and <GREY> on a VT52 are treated like <PF1>, <PF2> and <PF3>.
It is also possible to request commands with control keys (e.g. <CTRL/G>).
With a VT2+ keyboard you can also define the Function Keys <F6>..<F20> and <FIND>, <INSERT HERE> etc., but only when VT2plus support is included.
With a VT4+ <F1>..<F5> can be defined when this support is included.
The keys of a Tandberg TDV2230 keyboard can be defined like the ones on a VT2+, but only when TDV2230 support is included.
Define the command translation as “<key> := command”, for example:
+>PF2 := TIM	Redefine <PF2> or <RED> key
+><PF2>	to display the current time

+>F6 := ACT	Define F6 function key
+><F6>	to display the active tasks

The keys <FIND> etc. on a VT2+ keyboard must be entered as F$a where “a” is the first character of the key function (English key names), e.g.:
F$P	for <PREV-SCREEN>

Define a control key as follows:
+>^G := SET /UIC	Define <CTRL/G> key
+><CTRL/G>	to display the current UIC

Note that the following control-keys CAN NOT be defined:
<CTRL/M> ( = <RETURN> )
<CTRL/O>
<CTRL/Q>
<CTRL/S>
<CTRL/[> ( = <ESC> )

In addition to the remaining <CTRL/A..Z>, the following keys can be defined:
<CTRL/\>
<CTRL/]>
<CTRL/^>
<CTRL/?>

Note: A user-defined key overrules the function that the key may already have for MCE.
# Internal Commands (MCE xxxx)
If a command line starts with “MCE” an Internal Command is assumed. Following the verb MCE a four-character action specifier defines the action wanted, e.g.:
MCE CLEA	this command clears the FIFO-buffer.

Here follows a list of all internal commands:
- MCE CHAIn [file]
- MCE CLEAr
- MCE CMSZ n
- MCE ECHO ON|OFF
- MCE EXIT
- MCE FISZ n
- MCE FREE
- MCE INSErt ON|OFF
- MCE KEYPad ON|OFF
- MCE LIST
- MCE LOCK
- MCE OVERstrike ON|OFF
- MCE PROMpt ON|OFF
- MCE PURGe
- MCE READ [file]
- MCE REPLace [file]
- MCE RING
- MCE STATusline [ON|OFF]
- MCE SVINternals ON|OFF
- MCE SVOLd ON|OFF
- MCE TIMOut n|ON|OFF
- MCE UPFind ON|OFF
- MCE USPRompt [UserPrompt]
- MCE VERSion
## MCE CHAIn [file]
Chain from one Init-File to another, that is start or continue reading commands from the specified file. This command is a synonym for MCE READ [file]. This command is only available when Init-File support is included in MCE.
## MCE CLEAr
This command deletes all commands currently in the FIFO-buffer.
## MCE CMSZ n
Changes minimal command size to “n”. Only command lines that are equal to or longer than “n” characters are stored in the FIFO-buffer. Set the length to 79 if for any reason you do not want to save commands. The default setting can be specified at MCE build time.
## MCE ECHO ON|OFF
When “ON”, MCE echoes command lines to the terminal. This is useful in Init-Files to display messages etc. or to see the translation of command synonyms. The default setting is “OFF” (see example in Appendix A).
## MCE EXIT
This exits the MCE task.
## MCE FISZ n
Changes the maximum number of command lines which can be saved in the FIFO buffer. Note that the actual number of lines that can be saved depends on the length of the commands and the available MCE pool space.
Information about MCE’s pool space can be obtained with the MCE FREE command. More pool space can be obtained by installing MCE with a larger increment: “INS $MCE/INC=xxx”. A value of 2400, which is the default value used during task building (linking), will be enough in most cases. If “n” is smaller than the active number of command lines stored, MCE deletes the oldest lines from the FIFO buffer until “n” is reached.
The default setting can be specified at MCE build time.
## MCE FREE
Displays MCE’s pool information as follows:
MCE – Pool:xxx:yyy:zz
where
xxx	= Size of largest block in bytes
yyy	= Total number of free bytes
zz	= Number of fragments
## MCE INSErt ON|OFF
When “ON”, MCE goes back to Insert mode when prompting for a new command. The default setting can be specified at MCE build time.
MCE INSErt ON	Switches Auto-Overwrite mode off.
MCE OVERwrite ON	Switches Auto-Insert mode off.
## MCE KEYPad ON|OFF
Set Keypad editing on or off (see EDT-Keypad editing). This command is only available when EDT‑Keypad support is included in MCE.
## MCE LIST
Makes command FIFO-buffer a list: <UP> and <DOWN> stop at the top and bottom of the FIFO. This is the default setting (see also the MCE RING command).
## MCE LOCK
The LOCK command prompts for a Password and verification and then locks the terminal until the password is typed again, much like the LOCK command of Digital’s Terminal servers. The maximum password-length is 8 characters.
This command is available only when Terminal Password locking support is included in MCE.
## MCE OVERwrite ON|OFF
When “ON”, MCE goes back to Overwrite mode when prompting for a new command. The default setting can be specified at MCE build time.
MCE OVERstrike ON	Switches Auto-Insert mode off.
MCE INSErt ON	Switches Auto-Overwrite mode off.
## MCE PROMpt ON|OFF
Switches Extended Prompt on or off. The default setting can be specified at MCE build time. This command is only available when Extended Prompt support is included in MCE.
## MCE PURGe
This command deletes all command synonyms currently from the synonym buffer.
## MCE READ [file]
Read command lines from the specified file. This command is only available when Init-File support is included in MCE.
## MCE REPLace [file]
Combines the MCE PURGe and MCE READ [file] commands. This command is only available when Init-File support is included in MCE.
## MCE RING
Makes command FIFO-buffer a ring: <UP> and <DOWN> roll through the buffer. The default setting is “LIST” (see also the MCE LIST command).
## MCE STATus [ON|OFF]
This command turns the Status Line on or off. When no option is specified a snapshot of the Status Line is displayed (see Status Line support.)
The default setting can be specified at MCE build time. This command is only available when Status Line support has been included in MCE.
## MCE SVINternals ON|OFF
When “ON”, Internal commands (command lines starting with “MCE”) are saved in the FIFO-buffer, When “OFF” these commands are not saved. The default setting can be specified at MCE build time.
## MCE SVOLd ON|OFF
When “ON”, an “old” command (retrieved from the FIFO-buffer) is saved again in the FIFO-buffer if it is not the newest in the FIFO. When “OFF”, “old” commands are not saved unless they are edited. The default setting can be specified at MCE build time.
## MCE TIMOut n|ON|OFF
This command allows you to change the time-out value in minutes that you specified during MCEBLD run. The value “n” may be anything in the range of 2 to 999. You may also enable or disable time-out with the ON|OFF parameter.
This command is only available when Settable Terminal Time-Out support is included in MCE.
## MCE UPFInd ON|OFF
Since Version 4.27 of MCE, <UP> does a <RECALL> function (like <FIND>) when there is something on the command line and the cursor is at the end of the line. This feature is included because many PC command line editors have that feature. This is the default. The user can change to the old behavior with the MCE UPFInd OFF command.
## MCE USPRompt [UserPrompt]
When “UserPrompt” is specified, MCE uses this argument as the new prompt. It can contain up to 20 characters. When “UserPrompt” is not specified MCE uses the default prompt again.
This command is only available when User Prompt support is included in MCE.
## MCE VERSion
Shows the MCE Version identification.
## Some notes on Init-Files
When no filename argument is specified in the CHAIn, READ and REPLace commands, the same filename convention is used as at startup: the files according to the current CLI are read, i.e. the command MCE REPLace results in a MCE restart, but the FIFO-buffer is kept. This is useful after a “SET TERMINAL <new-cli>” command.
When a “space” is given as filename, only SY:[CurDir]MCEINI.xxx or SYS$LOGIN:MCEINI.xxx is read (see Init-File support).
# Recall function
Recalling a command is done by entering the first part of a command which was previously executed, terminated by a RECALL keystroke. This will recall the last command already executed starting with the string entered. The command can be edited or executed by pressing the return key. A second RECALL keystroke searches further back in the FIFO-buffer. When no string is entered, the last defined string is taken.
Recall keystrokes are:
<FIND>
<ESC>Q
When anything is on the command line	: <UP>
In non EDT-Keypad mode	: <PF2> or <RED>
In EDT-Keypad mode	: <PF3> or <GREY>

For example, if the following commands were previously entered:
+>DIR MCE*.*
+>MAC @MCEASM
+>TKB @MCETKB
+>DMP X.DAT
+>TIM
then
+>D<RECALL>

will recall the last command line starting with “D”:
+>DMP X.DAT

another <RECALL> keystroke will recall an older command from the FIFO starting with “D”:
+>DIR MCE*.*
Similarly,
+>DI<RECALL>
will recall
+>DIR MCE*.*

Note: Since Version 4.27 of MCE, <UP> does a <RECALL> function when there is something on the command line and the cursor is at the end of the line. This feature is included because many PC command line editors have that feature. This is the default. The user can change to the old behavior with the MCE UPFInd OFF command.
# Help File
A help file named MCE.HLP customized to the selected options is created when MCE is built.
Note that if you do not build the help file together with MCE, you cannot use the <NEXT‑SCREEN> and <PREV‑SCREEN> keys to walk through the help file.
# Line-Editing commands
Line-editing is done in one of two modes:
- Non-keypad mode
- Keypad mode
In the non-keypad mode, you control MCE with control keys or Escape sequences. In the keypad mode you can use the keypad of a VT52, VT1xx or a VT2+ terminal for additional edit operations.
The advantage of this mode is that you can edit the current command line in the same way as you edit a line in K52, KED or EDT.
## Non-keypad editing and cursor movement commands

Cursor movements
Move Cursor Left	<LEFT> / <CTRL/D>
Move Cursor Right	<RIGHT> / <CTRL/F>
Move Cursor to Begin Of Line (BOL)	<BACKSPACE> / <CTRL/H> / <F12>[5]
Move Cursor to End Of Line (EOL)	<CTRL/E>
Move one Word to the right or move from EOL to BOL	<TAB> / <CTRL/I>
[5] On a VT2+ terminal only when VT2plus support is included

Delete commands
Delete Character Left of Cursor	<DELETE>
Delete Character at Cursor	<CTRL/V>
Delete Word Left of Cursor	<LINEFEED> / <CTRL/J> / <F13>
Delete Word Right at Cursor	<CTRL/W>
Delete from Cursor to BOL	<CTRL/U>
Delete from Cursor to EOL	<CTRL/K>
Delete whole line	<CTRL/C>

Control commands
Rewrite Line	<CTRL/R>
Switch between Overwrite and Insert mode	<CTRL/A> / <F14>

Save and execute
Execute command	<RETURN> / <ENTER>
Execute command without waiting	<ESC><ESC> / <DO>
Execute command and leave FIFO-pointer where it is	<CTRL/X>
Save command without executing	<CTRL/N>
Enable output from other tasks. Detach for 10 sec.	<CTRL/T>
Enable output from other tasks. Stop; Resume with “UNS MCE”	<CTRL/P>

Non-keypad Command buffer manipulation keys
Display contents of FIFO-buffer	<PF4> / <ESC>S
Retrieve previous command	<UP> / <CTRL/B>
Reverse of <UP> (next command)	<DOWN>
Recall command from FIFO	<PF2> / <RED> / <FIND> / <ESC>Q / <UP> [6]
[6] See "MCE UPFInd" command

Non-keypad Help keys
Display HELP about MCE	<HELP> / <CTRL/?>
Display Next HELP screen	<NEXT-SCR>
Display Previous HELP screen	<PREV-SCR>

Non-keypad Command translation keys
Translate command synonym without execution	<PF1> / <BLUE> / <ESC>P
Show command synonym buffer	<PF3> / <GREY> / <ESC>R

## EDT-keypad editing and cursor movement commands
While in keypad-mode the non-keypad commands are valid, except those commands that are redefined.
### VT2+ Keyboard Lay-out

F11	F12	F13	F14		HELP	DO
(ESC)	(BS) / BEGLIN	(LF) DELWRD RIGHT	INS/OVR		HELP	EXECUTE NOWAIT

				PF1	PF2	PF3	PF4
(FIND) RECALL	INSERT HERE	REMOVE		GOLD	KPHELP	RECALL	DELLIN / UNDLIN
SELECT	PREV / HELP / (SCREEN)	NEXT HELP / (SCREEN)		TRANSL	SHOSYN / VERS	SHOFIF / FREE	DELWRD / UNDWRD
	PREV / COMM.			DETACH / SUSPND		CUT / PASTE	DELCHR / UNDCHR
<==	NEXT / COMM.	==>		WORD	EOL / DELLIN	DO STAY	ENTER
				BEGLIN / CLRLIN		SELECT / RESET	SAVE

### VT1xx Keypad Lay-out

UP	DOWN	LEFT	RIGHT
PREV. / COMM.	NEXT / CPMM.	<==	==>

PF1	PF2	PF3	PF4
GOLD	KPHELP	RECALL	DELLIN / UNDLIN
TRANSL	SHOSYN / VERS	SHOFIF / FREE	DELWRD / UNDWRD
DETACH / SUSPND		CUT / PASTE	DELCHR / UNDCHR
WORD	EOL / DELLIN	DO STAY	ENTER
BEGLIN / CLRLIN		SELECT / RESET	SAVE

### VT52 Keypad Lay-out

BLUE	RED	GREY	UP
GOLD	KPHELP	RECALL	PREV / COMM.
TRANSL	SHOSYN / VERS	SHOFIF / FREE	NEXT / COMM.
DETACH / SUSPND		CUT / PASTE	==>
WORD	EOL / DELLIN	DO STAY	<==
BEGLIN / CLRLIN		SELECT / RESET	ENTER / SAVE

### Keypad editing and cursormovement keys

Note : <KPx> means key x on the keypad.

Control commands
Select lower function	<PF1> / <BLUE>	GOLD

Cursormovements
Move Cursor to Begin Of Line	<KP0>	BEGLIN
Move Cursor to End Of Line	<KP2>	EOL
Move one Word to the right or move from EOL to BOL	<KP1>	WORD

Delete commands
Delete Character at Cursor	<KP,>	DELCHR
Delete Word Right at Cursor	<KP->	DELWRD
Delete from Cursor to EOL	<PF4> / <BLUE><KP2> / <PF1><KP2>	DELLIN
Delete Whole line	<PF1><KP0> / <BLUE><KP0>	CLRLIN

Undelete commands
Undelete Character	<PF1><KP,>	UNDCHR
Undelete Word	<PF1><KP->	UNDWRD
Undelete Line	<PF1><PF4>	UNDLIN

Cut and paste commands
Set Begin Of Textmarker BOT	<SELECT> / <KP.>	SELECT
Remove text from BOT to cursor and store it in the pastebuffer	<REMOVE> / <KP6>	CUT
Insert text-string from pastebuffer starting at cursor	<INSERT> / <BLUE><KP6> / <PF1><KP6>	PASTE
Reset selected range	<PF1><KP.> <BLUE><KP.>	RESET

Save and execute
Execute Command	<ENTER>	EXECUTE
Execute Cmd and leave FIFO-pointer where it is	<KP3>	DO-STAY
Save Command without executing	<PF1><ENTER> <BLUE><ENTER>	SAVE
Enable output from other tasks Detach for 10 sec.	<KP4>	DETACH
Enable output from other tasks Stop; Resume with “UNST MCE”	<PF1><KP4> <BLUE><KP4>	SUSPND

Command buffer manipulation keys
Display contents of FIFO-buffer	<KP9>	SHOFIF
Recall Command from FIFO	<PF3> / <GREY>	RECALL

Command translation keys
Translate Command synonym without execution	<KP7>	TRANSL
Show Command Synonym Buffer	<KP8>	SHOSYN

Miscellaneous keys
|Show version	<PF1><KP8> / <BLUE><KP8>	VERS
Show free pool	<PF1><KP9> / <BLUE><KP9>	FREE
Keypad Lay-out	<PF2> / <RED>	KPHELP

# Building MCE

This section deals with the generation of the MCE-task. The distribution contains the following files.

- MCE.MAC	Macro source file
- MCEBLD.CMD	ICP commandfile to build MCE
- MCEREL.TXT	Release notes
- MCE.DOC	This manual in Microsoft Word 6.0 format

To build The MCE-task you need the following files :

- MCE.MAC
- MCEBLD.CMD
- LB:[1,1]VMLIB.OLB

You start the building by typing :

@MCEBLD	(works with MCR and DCL)

Next you are asked to answer questions about which options you want to be included in MCE. The questions that are asked are about :

- MULTIPLE CLI SUPPORT
- INIT-FILE SUPPORT
- COMPOUND COMMANDLINE SUPPORT
- STATUSLINE SUPPORT
- STARTUP AND EXIT MESSAGES
- TYPE OF RT: AND HT: DETECTION
- VT2plus SUPPORT
- VT4plus SUPPORT
- TANDBERG TDV2230 SUPPORT
- EDT-KEYPAD SUPPORT
- USER PROMPT SUPPORT
- EXTENDED PROMPT SUPPORT
- TERMINAL PASSWORD LOCKING
- AUTO INSERT/OVERSTRIKE DEFAULTS
- SAVE OLD COMMANDS DEFAULT
- SAVE INTERNAL COMMANDS DEFAULT
- TERMINAL TIME-OUT SUPPORT
- MINIMAL CMD-LINE LENGTH
- MAXIMUM ENTRIES IN FIFO
- HELP FILE

MCEBLD.CMD creates the following files:

- MCESAVED.DAT	Saved Answers
- MCE.HLP	Help file
- MCEPRE.MAC	Conditional assembly prefix file
- MCEASM.CMD	MACRO commandfile
- MCETKB.CMD	TKB/LINK commandfile

Than MCEBLD.CMD invokes:

MAC @MCEASM
TKB @MCETKB or LINK @MCETKB

When present MCE will be built with FCSFSL.STB or FCSRES.STB

Sample build-sessions can be found in Appendices B and C
# Known problems

## DCL and installed tasks

MCE has some problems with DCL and installed tasks. DCL does not wait for installed tasks to complete. Compare the two examples below:

MCR	DCL
+>INS $FOO/TASK=FOO	+$ INS $FOO/TASK=FOO
+>RUN FOO	+$ RUN FOO
>	+$

 To solve this add the following line to MCEINI.DCL :

R*UN := RUN ‘P1’/STATUS:TASK

## MCE on RT:, HT: and LAT terminals

A terminal on an RT:, HT: or LAT line that has a task running that attaches the terminal can give some problems. When the line becomes disconnected by network Time-Out’s or manual interference the system tries to log-out the line.
On those lines BYE can not do I/O if the attached task has a priority higher than BYE. This is an RSX problem. MCE is a task that attaches the terminal and can give problems as mentioned. If BYE is installed with a higher priority than MCE (e.g. MCE 60 and BYE 70) the problem with MCE is solved.

## Remarks on 8-Bit terminals and lines

A VT2+ terminal in 7-bit mode always sends “normal” Escape-sequences :

PF1 = ESC [ P	(33, 133, 120)
F20 = ESC ? 3 4 ~	(33, 77, 63, 64, 176)

The EBC, RPA, PASTHRU settings of the TI: do not have effect on the processing of those keys.

A VT2+ terminal in 8-bit mode sends other sequences :

PF1 = SS3 P	(217, 120)
F20 = CSI 3 4 ~	(233, 63, 64, 176)

In this case the EBC, RPA, PASTHRU settings of the TI: do have effect. Although they do different things one of the options MUST be set to “on” to let MCE see the keypad keys the right way.
The IO.RST used by MCE sees the following terminating characters in IOSTB+1 :

EBC	RPA	PASTHRU	SS3	CSI	MCE
0	0	0	0	33	not OK
0	0	1	17	33	OK
0	1	0	17	33	OK
0	1	1	17	33	OK
1	0	0	217	233	OK
1	0	1	217	233	OK
1	1	0	217	233	OK
1	1	1	217	233	OK

Note : Always look at the release notes in MCEREL.TXT to see the latest information.

APPENDIX A

Example of an Init-File

!
! LB:[SYSTEM]MCEINI.MCR
!
        MCE STATUS ON
        MCE SVINTERN OFF
        MCE USPROMPT Oldie>
!
        ? := HELP
        AS*SEMBLE := MAC @'P1'ASM
        CO*PY := PIP 'P2'/NV='P1'
        D*IR := DIR
        FO := FOR @'P1'FTN
        F20 := CLR
        LI*NK := TKB @'P1'TKB
        MO*VE := PIP 'P2'/NV='P1' & PIP 'P1';0/DE/NM
        RE*NAME := PIP 'P2'='P1'/RE
        R*UN := RUN
        BLD := MAC @'P1'ASM & TKB @'P1'TKB
!
! Next command let you change to DCL and read the MCEINI.DCL file(s)
!
        GODCL := SET /DCL=TI: & MCE REPLACE
!
! MCR Commands...
!
        CLR ! Clear screen
        MCE ECHO ON ! Echo on
!
! ***WARNING*** -- The system will be down for PM next Friday
!
        MCE ECHO OFF ! Echo off
        TIM ! Show time and date
!
! End of LB:[SYSTEM]MCEINI.MCR
!
APPENDIX B

Sample MCE build-session (RSX-11M with MCR and no saved answers)

>@mcebld

       +---------------+
       | +-------+ |
       | / \ |
       | / D E C U S \ | D E C U S makes it work
       | \ P D P / |
       | \ S I G / |
       | +-------+ |
       +---------------+

MCEBLD.CMD -- Commandfile to build the MCE Commandline editor V4.28

 This Commandfile builds YOUR version of MCE. It prompts for several
 options to be build in MCE. It creates a conditional assembly
 definition file called MCEPRE.MAC, two Commandfiles MCEASM.CMD and
 MCETKB.CMD and optionally a helpfile MCE.HLP. If you already have those
 files you can restart MCEBLD with "@MCEBLD MAC" to assemble and
 taskbuild or "@MCEBLD LINK" to taskbuild.

*****

 MCEBLD can use saved answers from a previous session.

 MCEBLD can use the saved answers as default and still ask questions
 or it can directly use these answers and skip the questions which
 answers are defined.

MCEBLD -- Do you have a saved answer file [D:N] :

*****

 MCEBLD can save answers for a future session

MCEBLD -- Do you want to save answers [D:N] : y
MCEBLD -- Name of the saved answer file [D:MCESAVED.DAT] :

*****

 The standard CLI (Commandline Interpreter) of RSX is MCR.
 When your system supports the use of other CLIs such as DCL than
 include multiple CLI support in MCE.

MCEBLD -- Want the multiple CLI support [D:N] ? y

*****

 When Init-file support is included MCE reads initialization files
 which can contain Commanddefinitions Internal- and CLI-Commands.

 Files are searched in this order:

     LB:[1,2]MCEINI.xxx, followed by SY:[CurDir]MCEINI.xxx,

 where "xxx" is the name of the CLI defined for the terminal invoking
 MCE and "CurDir" is the default directory at the startup of MCE.

 This algorithm divides Commanddefinitions into 2 groups:
 A system-wide set in LB:[1,2], followed by a users private set.

MCEBLD -- Want the MCE Init-file support [D:N] ? y

*****

 MCE allows definitions of compound Commands.
 Using the ampersand (&) sign one can define an MCE Command as a
 sequence of multiple CLI Commands :

        E.g. +>STAT := TIM & PIP /LI & ACT /ALL ..... etc.

 or directly: E.g. +>MAC @TASKASM & TKB @TASKTKB

MCEBLD -- Want the compound Command support [D:N] ? y

*****

 It is possible to include statusline support.
 The statusline shows the different settings and FIFO-parameters of
 MCE and can be switched on/off with MCE STATus on/off
 Line 24 is used for status information.

MCEBLD -- Want Statusline/Statusmessage support [D:N] ? y
MCEBLD -- Want statusline ON by default [D:N] ?

*****

 The startup and exit messages like :

     "MCE -- CLI Commandline Editor V4.28" and "MCE -- Exit"

 are optional.

MCEBLD -- Want Startup and exit messages [D:N] ? y

*****

 When starting MCE via a remote terminal (RT: or HT:) problems may occur
 if the local system is VMS with its Commandline editor enabled.
 MCE can detect if it was started via a remote terminal and can do
 3 different things :

        1. Give the following message:

        MCE -- ** WARNING ** Started on a Remote Terminal.
        If your local system is OpenVMS with its Commandline
        editor enabled please type "MCE EXIT"

        2. Give the following message and exit :

        MCE -- Started on a Remote Terminal. Exiting .....

        3. Do nothing

MCEBLD -- Which option for RT: [D:1] : 2
MCEBLD -- Which option for HT: [D:1] : 2

*****

 VT2plus support enables the use of VT2xx, VT3xx, VT4xx and VT5xx
 terminals. The keys <F11>, <F12> and <F13> work as <ESC>, <BS> and
 <LF>. The keys <HELP>, <DO> etc. can also be used and it is possible
 to define the Functionkeys <F6>..<F20> like :

     "F6 := TIM"

 pushing <F6> gives the time of day then.

MCEBLD -- Want the VT2plus support [D:N] ? y

*****

 On a VT4xx and a VT5xx terminal it is possible to use <F1>..<F5> as
 normal Functionkeys.
 VT4plus support enables you to define those keys too if you answer "Y"
 to the following question.

MCEBLD -- Want the VT4plus support [D:N] ? y

*****

 The keys of a Tandberg TDV2230 terminal can also be defined.

MCEBLD -- Want the Tandberg TDV2230 function key support [D:N] ?

*****

 Some edit functions can be performed on the VTxxx keypad, similar
 to EDT, KED and K52.
 The Keypad-editing can be switched on/off with MCE KEYPad on/off

MCEBLD -- Want the EDT-Keypad editing support [D:N] ? y
MCEBLD -- Want EDT-Keypad editing ON by default [D:N] ? y

*****

 The MCE prompt can show if overstrike or insert mode is active
 by "+" and "-".
 It can also display if EDT-Keypad editing (when selected)
 is enabled when the statusline is off by ":"

     e.g. "+:>"

 The Extended Prompt can be switched on/off with MCE PROMpt on/off

MCEBLD -- Want the Extended Prompt [D:N] ? y
MCEBLD -- Want Extended Prompt ON by default [D:N] ? y

*****

 MCE can accept a User Prompt.
 This prompt can be specified with MCE USPRompt <UserPrompt>.
 The maximum prompt size is 20 characters.

MCEBLD -- Want the User Prompt [D:N] ? y

*****

 MCE can lock a terminal with a password.
 Almost like the LOCK Command from Digital's terminal servers.
 The maximum password-length is 8 characters.

MCEBLD -- Want the terminal password locking [D:N] ? y

*****

 By default overstrike or insert mode stays active until it is
 changed with <CTRL/A> or <F14>. MCE can be build so that it sets
 one of the modes active by default when it prompts for a new
 Command. This can be changed with the MCE INSErt on/off and the
 MCE OVERstrike on/off Commands.

MCEBLD -- Want MCE to set insert mode back by default [D:N] ? y

*****

 Default "old" Commands (retrieved from the FIFO and not edited) are
 saved again in the FIFO. MCE can be build so that it does not save
 them again.
 This mode can be changed with the MCE SVOLd on/off Command.

MCEBLD -- Want MCE to save "Old" Commands by default [D:N] ? y

*****

 Default internal Commands are saved in the FIFO. MCE can be build
 so that it does not save them.
 This mode can be changed with the MCE SVINtern on/off Command.

MCEBLD -- Want MCE to save Internal Commands by default [D:N] ? y

*****

 When terminal Time-Out support is included the terminal is logged
 out after a given Time-Out time (TT0: only exits MCE).
 Optionally you can select a fixed Time-Out time or select that the
 user can change the time.

MCEBLD -- Want the terminal Time-Out support [D:N] ? y
MCEBLD -- Want to enable the user to change the values [D:N] ? y
MCEBLD -- Enter default number of Time-Out minutes [2..999 D:4] : 360
MCEBLD -- Want the Time-Out to be ON by default [D:N] ? y

*****

 Only Commandlines with a length greater than or equal to a given
 length are saved in the FIFO.
 The value can be changed with the MCE CMSZ n Command.
 Use a value of 79 if you don't want to save at all.

MCEBLD -- Enter minimum Commandline length [1..79 D:4] : 1

*****

 Specify the default maximum number of Commands which can be saved
 in the FIFO. The value can be changed with the MCE FISZ n Command.
 Note that the actual number of Commands that can be saved depends
 on the size of the Commands and the available MCE pool space.
 Information about MCE's poolspace can be obtained by the
 MCE FREE Command.
 More poolspace can be created by installing MCE with a larger
 increment. INS $MCE/INC=xxx
 A value of 2400 will be enough in most cases.

MCEBLD -- Enter maximum number of entries in FIFO [1..99 D:22] : 18

*****

 A helpfile MCE.HLP customized to your selections is created
 dynamically if you answer "Y" to the following question.
 Note that if you don't build the helpfile now, you can't use
 the <NEXT-SCREEN> and <PREV-SCREEN> keys to walk through the helpfile.

MCEBLD -- Create helpfile on LB: [D:N] ? y

MCEBLD -- What is your Help Directory [D:[1,2]] :

*****

 The helpfile can be created in two different versions.

 VERSION 1 : You can access this one by typing HELP MCE [topic.....]
        but you have to include a reference like :
        1 MCE
        @MCE
        in MCR.HLP and DCL.HLP

 VERSION 2 : You can access this one by typing HELP /MCE [topic.....]
        This version does not need any editing of MCR.HLP and
        DCL.HLP

MCEBLD -- Do you want VERSION 2 [D:N] ? y

*****

MCEBLD -- When ready and successful copy MCE.TSK to LB: device [D:N] ? y
MCEBLD -- What is your Task Directory [D:[1,54]] :
MCEBLD -- Install task [D:N] ? y
MCEBLD -- Print listing and map [D:N] ?

MCEBLD -- All questions asked .....

MCEBLD -- Creating saved answer file MCESAVED.DAT
PIP MCESAVED.DAT/PU/NM
MCEBLD -- Creating helpfile LB:[1,2]MCE.HLP .....
PIP LB:[1,2]MCE.HLP/PU/NM
MCEBLD -- Creating configuration prefixfile MCEPRE.MAC .....
PIP MCEPRE.MAC/PU/NM
MCEBLD -- Creating MAC-Commandfile MCEASM.CMD .....
PIP MCEASM.CMD/PU/NM
MCEBLD -- Creating TKB-Commandfile MCETKB.CMD .....
PIP MCETKB.CMD/PU/NM
MCEBLD -- Assembling MCE .....
MAC @MCEASM
PIP MCE.OBJ/PU/NM,MCE.LST
MCEBLD -- Building MCE .....
TKB @MCETKB
PIP MCE.TSK/PU/NM,MCE.MAP
PIP LB:[1,54]/NV/FO/CO=MCE.TSK
ABO ...MCE
REM ...MCE
INS LB:[1,54]MCE
MCEBLD -- Procedure done
>
APPENDIX C

Sample MCE build-session (RSX-11M with MCR and saved answers)

>@mcebld

       +---------------+
       | +-------+ |
       | / \ |
       | / D E C U S \ | D E C U S makes it work
       | \ P D P / |
       | \ S I G / |
       | +-------+ |
       +---------------+

MCEBLD.CMD -- Commandfile to build the MCE Commandline editor V4.28

 This Commandfile builds YOUR version of MCE. It prompts for several
 options to be build in MCE. It creates a conditional assembly
 definition file called MCEPRE.MAC, two Commandfiles MCEASM.CMD and
 MCETKB.CMD and optionally a helpfile MCE.HLP. If you already have those
 files you can restart MCEBLD with "@MCEBLD MAC" to assemble and
 taskbuild or "@MCEBLD LINK" to taskbuild.

*****

 MCEBLD can use saved answers from a previous session.

 MCEBLD can use the saved answers as default and still ask questions
 or it can directly use these answers and skip the questions which
 answers are defined.

MCEBLD -- Do you have a saved answer file [D:N] : Y
MCEBLD -- Name of the saved answer file [D:MCESAVED.DAT] : [1,2]MCESAVED.DAT
MCEBLD -- Do you want to skip the questions [D:N] : Y

*****

 MCEBLD can save answers for a future session

MCEBLD -- Do you want to save answers [D:N] : Y
MCEBLD -- Name of the saved answer file [D:[1,2]MCESAVED.DAT] :

*****
        -- Multiple CLI support included : T
*****
        -- MCE Init-file support : T
*****
        -- Compound Command support : T
*****
        -- Statusline support : T
        -- Statusline ON by default : F
*****
        -- Startup and Exit messages support: T
*****
        -- RT messages : T
        -- RT Exit : F
        -- HT messages : T
        -- HT Exit : F
*****
        -- VT2plus support : T
*****
        -- VT4plus support : F
*****
        -- Tandberg TDV2230 support : F
*****
        -- EDT-Keypad support : T
        -- EDT-Keypad ON by default : T
*****
        -- Extended Prompt support : T
        -- Extended Prompt ON by default : T
*****
        -- User Prompt support : T
*****
        -- Password Locking : T
*****
        -- Insert mode default : T
        -- Overstrike mode default : F
*****
        -- Save OLD Commands : T
*****
        -- Save Internal Commands : T
*****
        -- Time-Out Support : T
        -- Time-Out Support change : T
        -- Time-Out value : 360
        -- Time-Out default ON : T

*****
        -- Minimum Commandline length : 1
*****
        -- Maximum FIFO length : 18

*****

 A helpfile MCE.HLP customized to your selections is created
 dynamically if you answer "Y" to the following question.
 Note that if you don't build the helpfile now, you can't use
 the <NEXT-SCREEN> and <PREV-SCREEN> keys to walk through the helpfile.

MCEBLD -- Create helpfile on LB: [D:Y] ?
        -- Help directory : [1,2]
*****
        -- VERSION 2 Helpfile : T

*****

MCEBLD -- When ready and successful copy MCE.TSK to LB: device [D:Y] ?
MCEBLD -- What is your Task Directory [D:[1,54]] :
MCEBLD -- Install task [D:Y] ?
MCEBLD -- Print listing and map [D:N] ?

MCEBLD -- Use the sourcefile [7,136]mce.mac [D:N] ? Y
MCEBLD -- All questions asked .....

MCEBLD -- Creating saved answer file MCESAVED.DAT
PIP MCESAVED.DAT/PU/NM
MCEBLD -- Creating helpfile LB:[1,2]MCE.HLP .....
PIP LB:[1,2]MCE.HLP/PU/NM
MCEBLD -- Creating configuration prefixfile MCEPRE.MAC .....
PIP MCEPRE.MAC/PU/NM
MCEBLD -- Creating MAC-command file MCEASM.CMD .....
PIP MCEASM.CMD/PU/NM
MCEBLD -- Creating TKB-command file MCETKB.CMD .....
PIP MCETKB.CMD/PU/NM
MCEBLD -- Assembling MCE .....
MAC @MCEASM
PIP MCE.OBJ/PU/NM,MCE.LST
MCEBLD -- Building MCE .....
TKB @MCETKB
PIP MCE.TSK/PU/NM,MCE.MAP
PIP LB:[1,54]/NV/FO/CO=MCE.TSK
INS LB:[1,54]MCE
MCEBLD -- Procedure done
>